## Slide 1: Town EOC Radio Comm
The Town EOC should have a VHF Base Radio Station
  Supported by a handful of portable radios
  With all frequencies to communicate with your first responders, the County and your adjacent towns
  Backup battery power for Base Station Radio
  Assigned Radio Operator(s)
Could also have a Amateur Radio capability
  FCC licensed Amateur Radio Operator
  Ham Radio Set or program your Base Station for locao VHF ham radio channels

## Slide 2: Before a Disaster
Know which county repeaters you can reach; test!
Know which other Town EOCs you can reach on a simplex channel; test!
Know what parts of your town you can reach on a simplex channel; test!

## Slide 3: BASIC OPERATING GUIDELINES
Ensure that you are on the channel you wish to transmit on.
Operate locally on your own frequency.
Monitor the County EMA Frequency.
Never make unnecessary transmissions. Always be brief and explicit.
Never use profanity on the radio.
Speak clearly to avoid the necessity to repeat.
Hold microphone close to and to the side of your mouth. (Speak across instead of into microphone)
Press the transmit button and wait a second before speaking.

## Slide 4: BASIC OPERATING GUIDELINES
Wait for breaks in conversations before speaking. If you must pass emergency information, use “Break, Break” terminology and state that information is important.
All transmissions will be in clear language.
Terminate and clear frequency promptly for others to use.
Give only information over the radio to perform the required official duties.
Never broadcast the name of deceased or injured over the air.
Spelling is sometimes used to clarify difficult words. Some letters sound much the same especially on the radio, so phonetic alphabets were developed in an attempt to identify letters with the word.

## Slide 5: RADIO MAINTENANCE
Try to run down a radio’s batteries before placing them in a charger.
Keep an extra set of batteries charged for immediate replacement.
Keep radios free of dirt and water. Wipe off with dry towel.
Never hold the radio by the antenna or clip anything to it. Never put any metal object on the antenna.